## Slide 1: Hydrology Rainfall-Runoff modelling: Pitman/WRMS 2000
Presented By: Sebastian Jahnke
Notes: WRC Logo

## Slide 2: Contents
Introduction and Overview
WRMS 2012 Resources
Collection and Collation of Input Data
Rainfall/Runoff Model
Calibration and Naturalisation of Flows
Conclusion

## Slide 3: Introduction and Overview

## Slide 4: Introduction and Overview
Originally developed in 1973 by Pitman (periodically updated)
Purpose: Simulate runoff from gauged/ ungauged catchments in South Africa/ Africa
Used for small and large catchments (developed and undeveloped scenarios)

## Slide 5: Introduction and Overview
Countries in which Pitman Model is used
Source: WRSM training

## Slide 6: Introduction and Overview
Rainfall/ Land Use data most important input to Water Resources Model(s)
Product of Pitman Model: Six major water resources assessments of South Africa conducted over last 7 decades
  E.g. WR90, WR2005 and WR2012 (Online Resources)

## Slide 7: Introduction and Overview
Rainfall/ Land Use data most important input to Water Resources Model(s) – decline in Rainfall Stations
Chart: Number of useful rainfall stations
?????

## Slide 8: Introduction and Overview
Usuthu Catchment example
Major decline in rainfall stations
Left with short/ ”patchy” rainfall datasets

## Slide 9: Introduction and Overview
Not only major decline in Rainfall Stations but also flow gauging stations
Chart: Year
Constant decline in Gauging stations

## Slide 10: Introduction and Overview
Major changes in Land Use and Water Requirements experienced over past decades
  Water use in South Africa grew from (estimated):
    3 500 million m3/a in 1953
    16 000 million m3/a in 2016
Reservoir Balances used as important planning instrument
  Records are deteriorating
  Many dams without records

## Slide 11: Introduction and Overview
Number of Reservoirs vs. Reservoir Records

## Slide 12: Introduction and Overview
Model consists of following modules:
  Surface- and Groundwater interaction (Runoff mod.)
  Afforestation (Commercial Forestry)
  Alien Vegetation (IAPs)
  Dryland crops
  Off Channel Wetlands
  Mining
  Irrigation

## Slide 13: WRMS 2012 Resources

## Slide 14: WRMS 2012 Resources
Pitman model used for country wide assessment
Website http://waterresourceswr2012.co.za/

## Slide 15: WRMS 2012 Resources
Resources menu available on website

## Slide 16: WRMS 2012 Resources
Download relevant material from the website (9GB) such as:
  Maps (download ArcViewer - freeware)
  Model Datasets
  Rainfall/ Gauging/ Water Quality Stations Data
  Land Use Data
  Reservoir Datasets
  Etc.

## Slide 17: WRMS 2012 Resources
Download relevant material from the website (9GB) such as:
  Maps (download ArcViewer - freeware)
  Model Datasets
  Rainfall/ Gauging/ Water Quality Stations Data
  Land Use Data
  Reservoir Datasets
  Etc.
Keep in mind that it was a high level country wide assessment – should be used by decision makers as overview instrument
Refine inputs for detailed studies

## Slide 18: WRMS 2012 Resources
Reference documents:
  WRSM2000 Theory Manual
  WRSM2000 Programmers Code Manual
  WRSM2012 User Manual
  WR2012 SALMOD
  WR2012 Groundwater Report
  WR2012 Executive Summary
  WR2012 Calibration Accuracy
  WR2012 Book of Maps
  Many more….
  (All included in the training material)

## Slide 19: Data Collection and Collation as Data Inputs

## Slide 20: Data Collection and Collation (Inputs)
Data requirements:
• Rainfall
• Evaporation
• Streamflow
• Groundwater use
• Irrigation
• Mines
Extensive detailed inputs are required
• Major/Minor reservoirs
• Alien invasive plants
• Forestry
• Geology
• Land Use Data

## Slide 21: Data Collection and Collation (Inputs)
Data requirements (cont.):
Important to maintain monitoring sites/equipment
Expand and improve measuring networks
  To measure is to know
Engage with stakeholders to obtain best possible water use data

## Slide 22: Rainfall/Runoff Model

## Slide 23: Rainfall/Runoff Model
Why:
Risk analysis (extreme drought)
Used if flow gauging network insufficient
Too short record periods and major changes in land use
To naturalise flow records (remove land-use effects)
Extend natural flow records (from rainfall)
Estimating flow in ungauged catchments (from neighbouring catchments)

## Slide 24: Rainfall/Runoff Model
Why:
Reservoir yield analysis
Conduct regional high level assessments of water resources, i.e. WR2012 study
Reserve Assessment and Determination
Input to WRYM, WRPM, WSAM and Water Quality Model

## Slide 25: Rainfall/Runoff Model

## Slide 26: Rainfall/Runoff Model
How (Process):
“Simplify” natural system by creating an equivalent network diagram (Step 1)
  Tertiary/Quaternary Catchment Resolution
  Describing the catchment linkages and water/land use
  Indicate where streamflow is measured (for calibration)
  5 different modules form network
  Routes joining the modules
    Loss free river reaches, canals or pipelines
    Each route has two modules – Source and Sink

## Slide 27: Rainfall/Runoff Model
Modules:
Runoff
Reservoir
Irrigation
Channel
Mining

## Slide 28: Rainfall/Runoff Model

## Slide 29: Rainfall/Runoff Model
Runoff Module
Main element of model
Provides streamflow to the system
  Catchment area,
  Rainfall,
  Evaporation,
  Calibration parameters, used to derive streamflow

## Slide 30: Rainfall/Runoff Model
Runoff Module (cont.)
Parent and Child (afforestation and alien vegetation)
Streamflow reduction area
Parent catchment
Child catchment e.g.
afforestation
Child catchment e.g alien vegetation
Riparian zone

## Slide 31: Rainfall/Runoff Model
Runoff Module (cont.)
Three different Runoff models available
  Pitman – as in original WRSM/Pitman – no surface/groundwater interaction
  Hughes – with surface/groundwater interaction, hence use Child module if appropriate
  Sami – same as for Hughes

## Slide 32: Rainfall/Runoff Model
Runoff Module (cont.)
Four different Afforestation models available
  Gush/ Pitman (ACRU) preferred
  Breakdown into three tree types
    Pine, Eucalyptus and Wattle

## Slide 33: Rainfall/Runoff Model
Runoff Module (cont.)
Alien vegetation
  Only CSIR option available
  Requires breakdown into 3 vegetation types
  (tall trees, medium trees and tall shrubs)
  Upland/riparian split to account for higher water loss in riparian area

## Slide 34: Rainfall/Runoff Model
Runoff Module

## Slide 35: Rainfall/Runoff Model
Reservoir Module
Can be large dam or collections of smaller dams
Storage area relationship used as input
(varies over time)
Is affected by:
  Inflows
  Abstractions
  Releases
  Spillages
  Rainfall and evaporation

## Slide 36: Rainfall/Runoff Model
Reservoir Module (cont.)
Reservoir records used to determine water balance
For large dams simulated inflows calibrated against inflow records
Compare observed and simulated storage

## Slide 37: Rainfall/Runoff Model
Irrigation Modules
Irrigation schemes of any size
Major water user in South Africa  significant impact on available yield
Complex data requirements:
  Irrigation area, crop types, irrigation method, … etc.
Four different methods to analyse irrigation
Irrigation influences simulated low flows – used as calibration tool
Notes: Irrigation influences simulated low flows  adjust irrigation module and seasonality of water require.

## Slide 38: Rainfall/Runoff Model
Channel Modules
Used to connect:
  Abstraction and return flow modules
  Wetland modules
Hub for modules

## Slide 39: Rainfall/Runoff Model
Mining Module
Data inputs are extensive/ difficult to obtain
  Only used for large mines (major impact on water resources)
Three different types of mines can be modelled
  Underground
  Open Cast
  Slurry dumps

## Slide 40: Rainfall/Runoff Model
SAMI Groundwater Model
Procedure:
Run Pitman model first
Obtain best estimates of parameters shared between models
Enter required groundwater parameters in the “Sami GW” window
HGSL, GPOW and HGGW parameters should be entered in the “Calibration” screen

## Slide 41: Rainfall/Runoff Model
SAMI Groundwater Model (cont.)
Refer to User Groundwater Manual for more details

## Slide 42: Rainfall/Runoff Model
SAMI Groundwater Model (cont.)
Different colours have been chosen for the data input window to assist users in select appropriate data:
  Red : Data should not be changed unless there is a very good reason
  Blue : Data could be changed if better information is available
    White : Default should always be changed unless there is no information whatsoever
  (This will be covered in the tutorial)

## Slide 43: Rainfall/Runoff Model
SAMI Groundwater Model (cont.)

## Slide 44: Rainfall/Runoff Model
Comprehensive Wetland Model
Water body linked to the main river channel
Inflow from channel to wetland starts above a prescribed discharge (level) in channel
Evaporation losses and abstractions occur (same as reservoir)
Comprehensive inputs required

## Slide 45: Rainfall/Runoff Model
Comprehensive Wetland Model (cont.)
Qin
Qout
Qds
Qloc
Qabss
Qloc = Local inflow directly into wetland
Qus = Flow in river channel upstream of wetland
Qds = Flow in river channel downstream of wetland
Qin = Flow into wetland from river channel
Qout = Flow into river channel from wetland
Qabs = Rate of abstraction from wetland/off-channel storage
Notes: Simulate as dam in WRYM with high penalty downstream channel

## Slide 46: Rainfall/Runoff Model
Model Outputs:
Summary of flows, storages in routes and reservoirs
Graphs
Statistics
Shortages
Data for runoff (groundwater data), channels (wetland data) and mining modules (runoff, seepage, storage etc.)

## Slide 47: Rainfall/Runoff Model
Output graphs:
Monthly hydrograph: Outliers, range of flows, dry season recession (perennial rivers)
Annual hydrograph: Outliers, wet & dry sequences
Seasonal distribution: Seasonal pattern, baseflow
Gross yield curves: Flow during critical periods
Scatter diagram: Goodness-of-fit, outliers
Histogram: See cumulative frequency (easier to interpret)
Cumulative frequency: Baseflow (perennial rivers), percentage time of zero flow (intermittent rivers)

## Slide 48: Rainfall/Runoff Model

## Slide 49: Naturalisation and Calibration of Flows

## Slide 50: Naturalisation and Calibration of Flows
Naturalisation
Naturalisation is the exclusion of man-made influences from the catchment hydrology
  Dams, Irrigation, abstractions, return flows, paved areas and mines are removed and “virgin” hydrology is determined
Naturalised flows can be determined from the runoff sub-model

## Slide 51: Naturalisation and Calibration of Flows
Calibration makes use of route statistics window
Flow gauging station data
Model Outputs
Suggestions to improve calibration

## Slide 52: Naturalisation and Calibration of Flows
Statistical Good Fit
  Error in MAR and Mean (log) : < 4%
  Error in Std. Dev. (natural & log) : < 6%
  Error in Seasonal Index : < 8%

## Slide 53: Naturalisation and Calibration of Flows
Statistical Good Fit
  Error in MAR and Mean (log) : < 4%
  Error in Std. Dev. (natural & log) : < 6%
  Error in Seasonal Index : < 8%

## Slide 54: Naturalisation and Calibration of Flows
Calibration flow chart

## Slide 55: Conclusion

## Slide 56: Conclusion
Used for long-term planning of water resources and water supply for South Africa, Lesotho and Swaziland
Naturalised streamflow (etc.) determined for WRYM (analyse yields of dams)
Used to analyse droughts and flood events
Create catchment water balance
Add value in terms of uncertainty analysis

## Slide 57: THE END